## Slide 1
MACHINE LEARNING • 2nd REVIEW
Bayesian Deep Learning-Based SIC Failure Prediction and Reliability-Aware User Scheduling
for Imperfect-SIC NOMA Networks
Project Team
P. Kethan — 2520040033 P. Kireeti — 2520040034 B. Shanmukh Pranay — 2520040070
Course: 25SC2107E | Department of ECE A.Y. 2026–27 | Guide: Mr. N. Lava Prasad

## Slide 2
Problem Statement
02
Why the problem matters
NOMA allows multiple users to share the same time/frequency resources. At the receiver, SIC is required to separate superimposed signals.
Problem in imperfect SIC
Noise, interference, channel variation, channel-estimation error and decoding errors can make SIC unreliable. A failure can increase BER, outage and reduce useful throughput.
What our project tries to predict
Wireless conditions
SNR • channel • power • interference
SIC risk
Probability of cancellation failure
Uncertainty
How confident is the prediction?
Scheduling
Choose lower-risk user pairs
Machine Learning • 2nd Review

## Slide 3
Proposed Methodology / Algorithm
03
Core idea: predict SIC failure probability first, then use risk + uncertainty for pairing.
1. Generate / collect NOMA conditions
2. Preprocess + standardize
3. Train neural classifier neural classifier
4. Repeated inference: mean + uncertainty
5. Reliability-aware user pairing
Bayesian prediction
• One hidden layer: 32 ReLU units • Dropout = 0.25 during training/inference • 40 repeated predictions for uncertainty estimation • Mean probability = predicted SIC risk • Standard deviation = uncertainty
Reliability-aware cost
For each strong/weak candidate pair: pair cost = predicted failure probability + 0.50 × prediction uncertainty Minimum-cost matching is then selected.
Baseline
Conventional NOMA pairing: • Sort users by SNR • Pair strongest with weakest • Continue inward Both methods use the same near/far candidate pools.
Source: project implementation (prediction + scheduling modules)

## Slide 4
Dataset, Features and ML Model
04
Synthetic dataset generated from a physically motivated imperfect-SIC simulation.
60,000
synthetic SIC attempts
8
input features
80/20
train / test split
55
training epochs
40
Repeated predictions
32
hidden units
Input features
SNR • channel gain • received power • interference channel-estimation error • power gap • mobility • user distance
ML formulation
Binary supervised classification: target = SIC failure (0/1) StandardScaler → Dense(32, ReLU) → Dropout(0.25) → Sigmoid Training uses mini-batch gradient descent + binary cross-entropy.
Course alignment: supervised learning, preprocessing and classification evaluation

## Slide 5
Project Workflow / Implementation
05
End-to-end execution in main.py
Data generation
60,000 samples synthetic NOMA/SIC
Preprocessing
stratified split standardization
Model training
55 epochs BCE loss
Repeated prediction
40 repeated predictions mean + std
Scheduling
80 users 40 pairs
Evaluation
BER • outage throughput • reliability
Code modules
data_generation.py • preprocessing.py • bayesian_model.py • scheduling.py • performance.py • visualization.py
Source: project README + main.py

## Slide 6
Simulation / Experimental Setup
06
Channel / link simulation
Distance: 40–500 m Tx power: 18–32 dBm Noise: −100 dBm Interference sampled around −112 to −78 dBm Imperfect-SIC effects include estimation error, power gap and mobility.
Training setup
Seed = 42 Batch size = 128 Epochs = 55 Learning rate = 0.001 Standardized inputs Binary cross-entropy loss
Evaluation
Prediction: accuracy, ROC-AUC, Brier score, mean uncertainty Scheduling: SIC failure rate, BER, outage, throughput and reliability 80 users → 40 scheduled pairs
Training loss decreases across 55 epochs.
Prediction standard deviation is used as prediction uncertainty.
Actual plots generated by the submitted project code

## Slide 7
Experimental Results: SIC Failure Predictor
07
Test-set results from the current implementation
0.846
test accuracy
0.928
ROC-AUC
0.122
Brier score
0.097
mean prediction std.
What the results show
• The model separates failure / non-failure cases with ROC-AUC ≈ 0.93. • Accuracy is ≈ 84.6% on the held-out test set. • Brier score is included because the system uses probabilities, not only class labels. • Repeated predictions provide an uncertainty estimate for downstream scheduling.
Important limitation at this stage
The dataset is synthetic and generated by the project simulation model. Therefore, these numbers demonstrate the implemented pipeline rather than validated performance on a real wireless-network dataset.
Actual test metrics: outputs/metrics/model_metrics.json

## Slide 8
Experimental Results: User Scheduling
08
Current run — 40 scheduled pairs
Metric
Conventional
Reliability-aware
Pred. SIC failure
0.190
0.108
Observed SIC failure
0.075
0.000
BER
0.069
0.039
Outage
0.150
0.075
Throughput (Mbps)
36.06
37.39
Reliability
0.850
0.925
Observation from this run
Reliability-aware pairing reduced predicted risk and improved the measured reliability/throughput metrics.
Actual comparison: outputs/metrics/final_comparison.csv

## Slide 9
Current Progress and Remaining Work
09
Completed / working
Synthetic imperfect-SIC dataset generation
Feature preprocessing and standardization
SIC failure predictor with uncertainty estimation
Uncertainty estimation using repeated stochastic inference
Conventional and reliability-aware NOMA pairing
BER / outage / throughput / reliability evaluation
Training, uncertainty and scheduling plots generated
Remaining / next stage
Test with a larger / real-world wireless dataset or validated simulator
Run repeated trials and report mean ± standard deviation
Add stratified k-fold cross-validation and hyperparameter search
Calibrate predicted probabilities and include a reliability diagram
Study scheduler sensitivity to the uncertainty weight (0.50)
Improve documentation, visualisation and final demonstration
2nd Review status: End-to-end prototype + initial experimental results completed; validation and refinement remain.
Aligned with course topics: evaluation, calibration, CV and ML engineering