## Slide 1
FINAL PROJECT | MACHINE LEARNING
Bayesian Deep Learning-Based SIC Failure Prediction
Reliability-Aware User Scheduling for Imperfect-SIC NOMA Networks
Course: 25SC2107E • Department of ECE • A.Y. 2026–27
Project team: [Add names and roll numbers]
Guide: [Add guide name]
FINAL PROJECT

## Slide 2
Project Overview
Abstract • the complete idea in one slide
FINAL PRESENTATION • 02/15
Objective
Estimate the likelihood of Successive Interference Cancellation (SIC) failure under imperfect NOMA conditions, then use prediction risk and uncertainty to guide user pairing.
Approach
A supervised neural classifier learns from simulated wireless-condition features. Repeated stochastic predictions provide a mean risk estimate and a prediction-standard-deviation measure. A cost-based scheduler selects lower-risk pairs.
CURRENT PROTOTYPE
0.928
ROC–AUC
0.925
Reliability*
*From one 40-pair scheduling run. Results are preliminary and based on synthetic data.
Focus: a working prediction-to-scheduling pipeline, with further validation still required.

## Slide 3
Background: NOMA and Imperfect SIC
Why the receiver needs reliable cancellation
FINAL PRESENTATION • 03/15
1 NOMA transmission
• Multiple users share time/frequency resources
• Signals are superimposed using different power levels
2 SIC receiver
• Receiver decodes a signal and subtracts it
• Residual interference remains if decoding/cancellation is imperfect
3 Network impact
• SIC failure can raise BER and outage
• Useful throughput and reliability may decrease
Sources of imperfect SIC in our simulation
Noise
Interference
Channel variation
Estimation error
Power gap
Mobility
Motivation: use estimated failure risk before committing users to pairs.

## Slide 4
Problem Definition & Objectives
What the project is designed to solve
FINAL PRESENTATION • 04/15
Problem
• Conventional pairing rules do not directly use a learned SIC-failure probability
• A probability estimate alone may hide prediction instability
• Scheduling decisions should account for both estimated risk and uncertainty
Objectives
• Train a binary classifier for SIC failure / non-failure
• Estimate uncertainty using repeated stochastic inference
• Define a risk-plus-uncertainty cost for candidate pairs
• Compare the proposed scheduler with an SNR-based baseline
Research question: does uncertainty-aware pairing improve simulated reliability metrics?

## Slide 5
Proposed System Architecture
The final pipeline implemented in the project code
FINAL PRESENTATION • 05/15
01
Synthetic SIC data
60,000 samples
02
Preprocessing
80/20 split standardization
03
Train classifier
32 ReLU units sigmoid output
04
Repeated inference
Mean risk + std.
05
Pair scheduling
Risk + uncertainty
06
Evaluate
BER / outage / rate
Code organization
data_generation.py • preprocessing.py • bayesian_model.py • scheduling.py • performance.py • visualization.py
main.py orchestrates the end-to-end run.

## Slide 6
Dataset and Model Implementation
Feature inputs, training configuration and prediction output
FINAL PRESENTATION • 06/15
60,000
synthetic attempts
8
input features
55
epochs
128
batch size
0.001
learning rate
Features used
• SNR, channel gain, received power, interference
• Channel-estimation error and power gap
• Mobility and user distance
Classifier configuration
• StandardScaler → Dense(32, ReLU)
• Dropout(0.25) → Sigmoid output
• Binary cross-entropy; stratified 80/20 split; seed 42
Label: SIC failure (0/1). The data are synthetic, generated by the project’s imperfect-SIC simulation.

## Slide 7
Uncertainty Estimation with Repeated Inference
How one trained network gives both a risk estimate and a confidence signal
FINAL PRESENTATION • 07/15
01
Input features
One user pair's 8 wireless features, standardized
02
Stochastic passes
Dropout(0.25) stays active; the pair is predicted T times
03
Set of predictions
One failure probability per pass; the values differ slightly
04
Risk + uncertainty
Mean → P̂ (risk) | Std. dev. → U (uncertainty)
WHAT IS COMPUTED
P̂ = (1/T) Σ pₜ
U = √[ (1/T) Σ (pₜ − P̂)² ]
These two numbers feed the pair cost.
Why U matters
• Two pairs can share the same P̂ but differ in stability
• Large U flags a prediction the model is unsure about
• Cost penalises both risk and uncertainty (weight 0.50)
Measured on the test set: mean prediction std. = 0.097. Repeated passes approximate Bayesian predictive uncertainty.

## Slide 8
Reliability-Aware Scheduling Algorithm
The scheduler uses predicted failure probability and uncertainty
FINAL PRESENTATION • 08/15
PAIR COST
Cᵢⱼ = P̂(SIC failure) + 0.50 × U
P̂ = mean predicted failure probability U = prediction standard deviation
Choose a minimum-cost matching.
Conventional baseline
• Sort users by SNR; pair strongest with weakest, then continue inward
Reliability-aware method
• Score candidate pairs using risk + uncertainty, then select lower-cost matches
Evaluation setup: 80 users → 40 pairs
The weight 0.50 is a design setting; sensitivity testing is future work.

## Slide 9
Scheduling Walk-Through
From 80 users to 40 NOMA pairs in one scheduling round
FINAL PRESENTATION • 09/15
1
Enumerate candidates
80 users can form up to 3,160 distinct pairs (80 choose 2).
2
Predict risk
The classifier gives each pair a mean failure probability P̂ and uncertainty U.
3
Score and match
Cost Cᵢⱼ = P̂ + 0.50 × U; a minimum-cost matching puts every user in exactly one pair.
4
Evaluate
Simulate both schedules on the same 80 users; record failure, BER, outage, rate, reliability.
SAME SCENARIO, TWO RULES
80 → 40
users → pairs
Baseline
Sort by SNR; pair strongest with weakest, then inward
Reliability-aware
Pick lower-cost pairs from risk + uncertainty
Only the pairing rule changes between the two methods, so the metric differences come from scheduling.

## Slide 10
Experimental Setup & Evaluation Metrics
Simulation ranges and how performance is measured
FINAL PRESENTATION • 10/15
Wireless simulation
• User distance: 40–500 m
• Transmit power: 18–32 dBm
• Noise power: −100 dBm
• Interference sampled around −112 to −78 dBm
• Imperfect-SIC effects include estimation error, power gap and mobility
Evaluation metrics
• Predictor: accuracy, ROC–AUC, Brier score and mean prediction standard deviation
• Scheduler: predicted/observed SIC failure, BER, outage, throughput and reliability
• Baseline and proposed method evaluated using the same 80-user scenario
Classification
Probability quality
Link performance
Reliability
Results below are from the current implementation and one stochastic scheduling run.

## Slide 11
Results & Performance Comparison
Predictor test metrics and current 40-pair scheduling run
FINAL PRESENTATION • 11/15
A. SIC failure prediction
84.6%
test accuracy
0.928
ROC–AUC
0.122
Brier score
0.097
mean prediction std.
B. Scheduling comparison
Metric
Conventional
Reliability-aware
Observed SIC failure
7.5%
0.0%
BER
0.069
0.039
Outage
15.0%
7.5%
Throughput
36.06 Mbps
37.39 Mbps
Reliability
0.850
0.925
Interpretation: this run favoured reliability-aware scheduling. Because the run is stochastic and the data are synthetic, repeat trials are needed before claiming general improvement.

## Slide 12
Model Evaluation Plots
Calibration, epistemic uncertainty and error rate from the project outputs
FINAL PRESENTATION • 12/15
Reliability diagram
DeepEnsemble stays close to the ideal diagonal; LogReg deviates in the mid-range
Epistemic uncertainty
Shifted (bad CSI) inputs show a wider, higher mutual-information spread
Error vs uncertainty
Misclassification rises from ~0 in low quintiles to ~12% in the top quintile

## Slide 13
Key Findings & Discussion
What the current evidence supports, and what it does not yet show
FINAL PRESENTATION • 13/15
0.928
predictor ROC–AUC
Risk score separates failure from non-failure well
3 → 0
pairs failing SIC
7.5% of 40 pairs became 0.0%
6 → 3
pairs in outage
15.0% fell to 7.5%
0.925
reliability
Up from 0.850 under the SNR baseline
What supports the approach
• Lower predicted risk translated into fewer observed failures
• BER and outage both improved, not only one metric
• Throughput also rose, so reliability gains did not cost rate in this run
What we cannot yet claim
• Results come from one stochastic run of 40 pairs
• Data are synthetic, so real-network gains are untested
• The contribution of U alone is not isolated (no ablation yet)
Takeaway: a promising prototype result that motivates repeated trials, not a proven improvement.

## Slide 14
Limitations & Validity Considerations
Where the prototype is limited, and the planned remedy for each point
FINAL PRESENTATION • 14/15
LIMITATION
PLANNED REMEDY
Synthetic data
Simulated imperfect-SIC conditions may not match real channels
Validate on a larger dataset or an independently verified simulator
Single scheduling run
One stochastic run of 40 pairs gives no variance estimate
Repeat trials and report mean ± standard deviation
Fixed uncertainty weight
The 0.50 weight in the pair cost is a design choice
Run a sensitivity sweep over the weight
Probability calibration
Accuracy is from one 80/20 split; calibration is unchecked
Stratified k-fold cross-validation and calibration analysis
These are the same steps listed under Future Work on the final slide.

## Slide 15
CONCLUSION & FUTURE WORK
Prediction informs scheduling. Uncertainty adds caution.
The project delivers an end-to-end prototype that predicts SIC failure risk and uses risk plus prediction uncertainty to form NOMA user pairs.
NEXT STEPS
• Evaluate on a larger dataset or independently validated simulator
• Run repeated trials and report mean ± standard deviation
• Add stratified k-fold cross-validation and probability calibration
• Study sensitivity to the uncertainty weight
Thank you • Questions?
FINAL PRESENTATION • 15/15